## Slide 1: Looking ahead: EPAC and data management
Stephen Dann (Central Laser Facility)

## Slide 2: Two sides of the CLF
High-Power Lasers
Lasers for Science
Gemini
12 J in 30 fs
1 shot per 20 s
Vulcan
400 J in 400 fs
1 shot per 20 minutes
Artemis
8 mJ in 30 fs
1 kHz
Ultra
Time-resolved spectroscopy
Octopus
Advanced imaging facility
I am here
Notes: Last year: Dan Rolfe of Octopus
Now: look at the other side of the CLF: HPL
Two facilities: Gemini and Vulcan. Mostly 5-6 week experiments with academic users.
Both have low repetition rates, so small amounts of data

## Slide 3: Imaging with high-power lasers
Multi-modal
– electrons, x-rays, ions, neutrons, terahertz
Bright
– up to 1012 particles/photons per pulse
Ultra-short pulse
– of order femtoseconds - picoseconds
Small source size
–as small as a few μm
Notes: One key application
Use laser to generate other types of radiation; use that to image samples
Other facilities exist, but laser-driven sources have some key benefits:
Multiple types of radiation (reconfigurable or multi-modal)
Small source size for coherent imaging
Short pulse for temporal resolution

## Slide 4: Imaging at the CLF
Promising results
Low repetition rates
Busy experiment schedule
No dedicated equipment
X-ray CT with Betatron radiation
Flash radiography
Phase contrast imaging
Notes: Already have results from Gemini (and Vulcan), but hard to compete with other sources, so…

## Slide 5: Extreme Photonics Application Centre (EPAC)
Funded by UK government strategic priorities fund
Facility exploiting CLF’s proprietary DiPOLE technology for academic, industry and security users
D100 laser pumping a Ti:S amplifier, with an OPCPA front-end
30 J, 30 fs, 10 Hz
Online in 2024
😲
Notes: EPAC is a new £80M facility, currently under construction.
Looks like a bigger Gemini, but there’s a stronger focus on needs of industrial users
Key benefits over Gemini:
Higher repetition rate
Larger experimental areas
Streamlined experiments

## Slide 6: Dealing with big(ger) data
Acquisition and display
  On-premises hardware
  2-5 GB/s
Storage and analysis
  Collaboration with Scientific Computing Department
  Tape library
  Ceph cluster
  STFC cloud
Data access through common RAL platform:
  ISIS
  Diamond Light Source
  Central Laser Facility
Gemini: 2 TB / year
EPAC: 1 PB / year?
Notes: Higher rep rate brings new challenges: 200 times as much data?
Add new detectors and more efficient use of experimental time and the difference is even bigger
DAQ handled on-site: expect 2-5 GB/s when fully operational
Data storage and analysis uses h/w and s/w from the STFC Scientific Computing Department

## Slide 7: Data Sources
Laser diagnostics
~0.5 MB images
>100 cameras?
Radiation diagnostics
~10 MB images
~3 cameras
Main detectors
~30 MB images
~4 cameras
Time
Only a small fraction of laser diagnostics data will be saved
PIC
PIC
PIC
Cameras shown are representative examples
Notes: Most data: images
Lots of laser diagnostics, but no need to save most of that data
Radiation diagnostics monitor performance of radiation generation
Main detectors are used for actual imaging process – experimental data
Diagnostics more of interest to facility and some academic users

## Slide 8: Experimental data volumes
Radiation
300 MB/s
Main detectors: 1.2 GB/s
Laser
400 MB/s
Total: 1.9 GB/s
Current estimates for 10 Hz operation
Even larger detectors are possible
10 Gb/s (for scale)
Diagnostics
Notes: Imaging detectors make up most of the data, due to sheer size
Could throw away other data: won’t help much

## Slide 9: External data flows
~10 TB/year
OperationsGateway
Long-term data storage for facility operations
Laser diagnostics
Radiation diagnostics
Main detectors
3 PB/year
1 PB/year
Data archive
Long-term data storage for experiments
“Interesting” data is kept
“Boring” data is discarded
Laser diagnostics
Radiation diagnostics
Subsample
Notes: Some diagnostic data is kept long-term for facility staff.
We can subsample this to keep data volumes manageable
Data for facility users is biggest challenge. Need curation by humans.
Example data rates:
3 PB/year produces
Only 1 PB/year can be kept
Users will need to choose which data to keep

## Slide 10: Data Storage and Analysis
Tape archive
(long-term storage)
Ceph cluster
(live data storage)
Data Analysis as a Service
(cloud-based analysis platform)
New data
EPAC
Scientific Computing Department
Not pictured: data cataloguing and access
To HPC?
Notes: Experimental data kept on SCD h/w.
Basic idea: Ceph cluster for data in-use, moved automatically to tape archive
Data restored from tape when needed
Data can be analysed directly in the cloud
Might also connect to HPC (e.g. SCARF)

## Slide 11: Data analysis
Analysis data
Experiment data
CPU
RAM
GPU
Software
User’s browser
Preinstalled software
Image processing tools
Scientific libraries
Special-purpose analysis packages
Tomography reconstruction
  Use GPUs!
Advanced CT methods
Iterative
Multi-modal
Higher-dimensional (e.g. time or energy resolved)
https://www.scd.stfc.ac.uk/Pages/Dynamic-Infrastructure-Group.aspx
Notes: VM in cloud provides access to compute hardware, data, and preinstalled software
Developed by Dynamic Infrastructure Group at RAL and used by ISIS and (parts of) CLF
Advanced CT reconstruction techniques need big GPUs: data set (typically) needs to fit in VRAM, and lots of system RAM needed too
Some types of CT (parallel-beam) are easy to split up into subproblems, but cone-beam and regularisation make that more difficult.
2k^3 reconstruction requires 32 GiB RAM with single-precision float

## Slide 12: Thank you