## Slide 1
Burkhard Schmidt, CERN
on behalf of the LHCb Collaboration
The LHCb upgrade

## Slide 2: Overview
Introduction to LHCb
LHCb upgrade
  Physics Motivation
  Trigger upgrade
  Detector upgrade
    Vertexing and tracking
    Particle Identification
Conclusions
LHCb Collaboration
~900 physicists
64 universities
16 countries

## Slide 3: Introduction
LHCb is a high precision experiment devoted to the search for New Physics (NP) beyond the Standard Model (SM)
Study CP violation and rare decays in the b and c-quark sectors
Search for deviations from the SM due to virtual contributions of new heavy particles in loop diagrams
Sensitive to new particles above the TeV scale not accessible to direct searches
Vertex Detector
reconstruct vertices
decay time resolution: 45 fs
IP resolution: 20 μm
Tracking system
momentum resolution
Δp/p = 0.4%–0.6%
RICH detectors
K/π/p separation
Dipole Magnet
bending power: 4 Tm
Calorimeters
energy measurement
e/γ identification
Muon system
μ identification

## Slide 4: Some highlights of LHCb results
PRD 87 (2013) 112010
Φs = 0.01 ± 0.07(stat) ± 0.01(syst)
B0 → K*0μ+μ-
1 fb-1
q02 = 4.9 ± 0.9 GeV2/c4
JHEP 1308 (2013) 131
γ = (67.2±12.0)°
from B→DK
LHCb-CONF-2013-006
PRL 111 (2013) 101805
BS0 → µ+µ ̶
Notes: CP violating phase φs in Bs mixing
Zero crossing point of the Fwd Bwd asymmetry in B0K*μ+μ- decays.

## Slide 5: Motivation for the LHCb upgrade
Present experimental status:
flavour changing processes are consistent with the CKM mechanism
large sources of flavour symmetry breaking are excluded at the TeV scale
the flavour structure of NP would be very peculiar at the TeV scale (MFV)
Why is the LHCb upgrade important:
measurable deviations from the SM are still expected, but should be small
need to go to high precision measurements to probe clean observables
 LHCb upgrade essential to increase statistical precision significantly
Quark flavour physics main component, but physics program includes also:
  Lepton flavour physics
  Electroweak physics
  Exotic searches, proton-ion physics
 Reinforce LHCb as general purpose forward detector

## Slide 6: LHCb upgrade
CERN-LHCC-2011-001
CERN-LHCC-2012-007

## Slide 7: Expected luminosity evolution
LHCb upgrade  ≥ 50 fb-1:
increase precision on quark flavour physics observables
aim at experimental sensitivities comparable to theoretical uncertainties
LHCb up to 2018  ~ 8 fb-1:
find or rule-out large sources of flavour symmetry breaking at the TeV scale
~
2011 2012 2013 2014 2015 2016 2017 2018 2019 2020 2021 2022 2023 2024 2025 2026
LHC Run I LS1 LHC Run II LS 2 LHC Run III LS3 LHC Run IV
pp runs with LHC splice pp runs with LHC injector pp runs with HL-LHC prep
- 50ns bunch spacing consoli- - 25ns bunch spacing, upgrade - 25ns b.spacing GPD phase 2
- ECM 7TeV and 8 TeV dation - ECM 13 TeV LHCb - ECM 14 TeV upgrades
LHCb L~4x1032/cm2/s LHCb L>4x1032/cm2/s upgrade L > 1x1033/cm2/s L=2x1033/cm2/s
LHCb ∫L ~3/fb LHCb ∫L >5/fb LHCb ∫L > 15/fb ∫L > 23/fb

## Slide 8: LHCb upgrade - expected precision
Bs mixing phase 𝜙s
q0 from B→K*ll
CKM angle 𝛾 from trees
A𝛤: CPV in charm
From M.H. Schune, ECFA HL-LHC 2013 workshop

## Slide 9: LHCb statistical sensitivity to flavour observables
Getting close to the theoretical uncertainties 8 fb-1 up to 2018
≥ 50 fb-1 for the upgrade
Framework TDR for the LHCb Upgrade
CERN-LHCC-2012-007
Notes: Expected statistical uncertainties on a few selected physics channels before and after the upgrade, compared to theory.
CP violating observables, rare decays and fundamental parameters of the CKM unitary triangle.

## Slide 10: Trigger upgrade
CERN-LHCC-2014-016

## Slide 11: LHCb Trigger – Limitations
Level -0
L0
e, g
40 MHz
L0
had
L0
m
Max 1 MHz
High-Level Trigger
Partial reconstruction
HLT1
Global reconstruction
30 kHz
HLT2
Inclusive selections
m, m+track, mm, topological, charm, ϕ
& Exclusive selections
3-5 kHz
Storage: event size ~60kB
Final states with muons
 Linear gain
Hadronic final states
 Yield flattens out ---
 Must raise pT cut to
stay within 1 MHz
readout limit
To profit of a luminosity of 1033cm-2s-1, information has to be introduced that is more discriminating than ET.
hardware
Upgrade strategy:
40MHz readout rate
Fully software trigger
20kHz output rate
software
LHCb 2012

## Slide 12: LHCb Trigger Upgrade
Effect on luminosity and signal yields
upgrade
Run I
Run II
Run III
Run IV
1/fb
run an efficient and selective software trigger with access to the full detector information at every 25 ns bunch crossing
increase luminosity and signal yields

30 MHz inelastic collision rate
to storage
(15 to) 30 MHz
LLT (optional)
(1 to) 2 MHz
Notes: Output rate 2-10 GB/s (20-100kHz)

## Slide 13: Detector upgrade to 40 MHz R/O
0 10 m 20 m
New VELO
(Vertex Locator)
New Tracking System
RICH Detectors:
Replace photodetectors and change RICH1 optics
Muon System
Replace ODE
Calorimeters
Replace R/O
upgrade ALL sub-systems to 40 MHz Front-End (FE) electronics
replace complete sub-systems with embedded FE electronics
adapt sub-systems to increased occupancies due to higher luminosity
keep excellent performance of sub-systems with 5 times higher luminosity
IP

## Slide 14: Vertex Detector Upgrade
Present detector and its performance
Detector upgrade
Expected Performance
CERN-LHCC-2013-021

## Slide 15: Current VErtex LOcator
Two retractable halves
5.5 mm from beam when closed
3o mm during injection
Operates in secondary vacuum
300 μm Al-foils separate detector from beam
21 R/ Φ modules per half
Silicon micro-strip sensors
Pitch 38-101 μm
Impact Parameter resolution (in x)

## Slide 16: VELO upgrade
tracks/chip/event at L=2∙1033 cm-2s-1
Upgrade challenge:
withstand increased radiation
(highly non-uniform radiation of up to 8∙1015 neq/cm2 for 50 fb-1)
handle high data volume
keep (improve) current performance
  lower materiel budget
  enlarge acceptance
Technical choices :
55x55 µm2 pixel sensors with micro channel CO2 cooling
40 MHz VELOPIX (evolution of TIMEPIX 3, Medipix)
130 nm technology to sustain ~400 MRad in 10 years
replace RF-foil between detector and beam vacuum
  reduce thickness from 300 μm → ≤ 250 μm
move closer to the beam
  reduce inner aperture from 5.5 mm → 3.5 mm
RF-foil
current inner aperture 5.5 mm
new aperture 3.5 mm
Notes: 8.5 tracks/chip/event correspond to a data-rate of 15 Gbit/s (no buffering).

## Slide 17: VELO upgrade
tracks/chip/event at L=2∙1033 cm-2s-1
Upgrade challenge:
withstand increased radiation
(highly non-uniform radiation of up to 8∙1015 neq/cm2 for 50 fb-1)
handle high data volume
keep (improve) current performance
  lower materiel budget
  enlarge acceptance
Technical choices :
55x55 µm2 pixel sensors with micro channel CO2 cooling
40 MHz VELOPIX (evolution of TIMEPIX 3, Medipix)
130 nm technology to sustain ~400 MRad in 10 years
replace RF-foil between detector and beam vacuum
  reduce thickness from 300 μm → ≤ 250 μm
move closer to the beam
  reduce inner aperture from 5.5 mm → 3.5 mm
Sensors
(front, back, bonds)
Micro channel cooling substrate
RF-foil

## Slide 18: VELO upgrade performance
better impact parameter resolution due to reduced material budget
reduced ghost rate
improved efficiency over pT, 𝜙, 𝜂
3D IP resolution at
L = 2∙1033 cm-2s-1
note: full GEANT Monte Carlo with standard LHCb simulation framework

## Slide 19: Tracker Upgrade
Upstream Tracker
Scintillating Fibre
Tracker
CERN-LHCC-2014-001

## Slide 20: Present Tracking System
σ = 7 MeV/c2
excellent mass resolution
very low background, comparable to e+e- machines
world’s best mass measurements [PLB 708 (2012) 241]
Trigger
Tracker
T-stations
TT silicon
IT silicon
OT straw tubes
Inner
Tracker
Outer
Tracker
TT

## Slide 21: TT upgrade: Upstream Tracker (UT)
GBT
GBT
40MHz silicon strip R/O  SALT chip
KAPTON TAPE
adapt segmentation to varying occupancies (out  in-side):
98  49 mm long strips
190  95 µm pitch
p+-in-n  n+-in-p
silicon strip detector
outer
middle
inner
SUPPORT
40MHz silicon strip R/O  SALT chip

## Slide 22: T-stations upgrade: Fibre Tracker
1 SiPM channel
Scint.-fibre mat (5-6 layers)
SiPM array
R/O by dedicated 128 ch. 40 MHz PACIFIC chip
3 thresholds (2 bits)
sum threshold (FPGA)
1.25 mm
2 x ~3 m
2 x ~ 2.5 m
fibre ends
mirrored
3 stations of X-U-V-X (±5o stereo angle) scintillating fibre planes
every plane made of 5 layers of Ø=250 µm fibres, 2.5 m long
40 MHz readout and Silicon PMs at periphery
Challenges: radiation environment
ionization damage to fibres  tested ok
neutron damage to SiPM  operate at -40oC
large size – high precision, O(10’000 km) of fibres
SiPM readout
SiPM readout
Benefits of SciFi concept:
a single technology to operate
uniform material budget
SiPM + infrastructure outside accept.
x-position resolution of 50 – 75 µm
fast pattern recognition for HLT
Notes: Photons create signal, fired pixels are red

## Slide 23: Tracking performance
OT
IT
SciFi
Efficiency for Bs → ΦΦ events:
upgrade conditions,
current and upgraded T-stations
Ghost rate for Bs → ΦΦ events:
long tracks without UT and
with UT (≥ 3hits)
with UT
without UT
improve tracking performance at upgrade luminosity with Fibre Tracker
reduce significantly the ghost rate using the Upstream Tracker information
Notes: Left plot illustrates the superior performance of the SciFi Tracker compared to the OT.
Adding UT hits has the advantage that the momentum resolution improves significantly.
Moreover, the requirement to have at least three UT hits reduces the ghost rate while keeping the efficiency.

## Slide 24: Tracking algorithm for the Trigger
Expected CPU budget with upgraded Event Filter Farm:
~13 ms (10 x current CPU farm)
 leaves ~ 6-7 ms for a trigger decision
Performance of HLT tracking with upgraded VELO, UT and FT:
GEC (Global Event Cut) → multiplicity cut to remove pathological events (e.g. hit multiplicity of sub-detector)
ms
 high efficiency (even with GEC)
Notes: Bottom table: track finding efficiencies.
B-daughter tracks have pT more than 500MeV.
Relative means relative to offline.

## Slide 25: Particle Identification Upgrade
RICH
Calorimeter
Muon System
CERN-LHCC-2013-001

## Slide 26: Particle ID with RICH
Bd0  π+ π-
particle identification of 2 π
BR(Bπ+π-) = 5 x 10-6 !
K-identification and π-misidentification efficiencies vs. particle momentum
B0  h+ h-
Bd0  π+ π-
Efficient particle ID of π, K, p essential for selecting rare beauty and charm decays
Eur. Phys. J. C (2013) 73:2431
Notes: Invariant mass distribution for B →h+h− decays in the LHCb data before the use of the RICH information (top), and after applying RICH particle identification (bottom).
The signal under study is the decay B0 → π+π−, represented by the turquoise dotted line.
The contributions from different b-hadron decay modes (B0 → Kπ red dashed-dotted line, B0 → 3-body orange dashed-dashed line, Bs →KK yellow line, Bs →Kπ brown line, Ʌb →pK purple line, Ʌb → pπ green line), are eliminated by positive identification of pions, kaons and protons and only the signal and two background contributions remain visible in the plot on the right. The grey solid line is the combinatorial background.

## Slide 27: Present RICH 1
C4F10
Hybrid Photon Detector
with embedded 1 MHz R/O chip
RICH 1
photon detectors
plane mirror
spherical mirror
HPDs
Particles traversing radiator produce Cherenkov light rings on an array of HPDs located outside the acceptance
Eur. Phys. J. C (2013) 73:2431
Notes: Reconstructed Cherenkov angle as a function of track momentum in the C4F10 radiator

## Slide 28: RICH upgrade
Luminosity of 2∙1033 cm-2s-1  adapt to high occupancies
aerogel radiator removed
modify optics of RICH1 to spread out Cherenkov rings (optimise gas enclosure without modifying B-shield)
40 MHz readout  replace HPDs due to embedded FE
64 ch. multi-anode PMTs (baseline)
40 MHz Front-End: CLARO chip (or MAROC)
Prototype of photo-detector readout module
64 ch. MaPMT
optimise RICH1 optics
current
upgrade

## Slide 29: Performance RICH upgrade
Current RICH1
2∙1032 cm-2s-1
10∙1032 cm-2s-1
20∙1032 cm-2s-1
RICH1 upgrade
20∙1032 cm-2s-1
Pion misidentification efficiency [%]
Kaon identification efficiency [%]
as function of luminosity
note:
full GEANT MC with standard LHCb simulation framework

## Slide 30: Particle ID with Calorimeters
Calorimeters allow to reconstruct neutral hadrons
They provide an ET measurement used in the LO trigger
Radiative b s γ transitions:
Invariant mass resolution ~ 94 MeV/c2
dominated by ECAL energy resolution.
Typical π0 mass resolution:
~7-10 MeV/c2 (depending on
number of converted photons)
π0 → γγ
Nuclear Physics, Section B 867 (2013) 1
B0→K*γ
Notes: The performance of high energy photon reconstruction is illustrated by the reconstructed B0  Ko γ mass distribution.
The mass resolution obtained for this radiative decay, 93 MeV=c2 is dominated by the ECAL energy resolution.
Reproducing the resolution of data with simulation samples, this corresponds to an intrinsic resolution in the photon energy of around 2%.

## Slide 31: Calorimeter upgrade
40 MHz readout electronics:
reduce photomultiplier gain
adopt electronics
Radiation damage on detectors:
Preshower and SPD removed
HCAL modules ok up to ~50 fb-1
irradiation tests show that most exposed ECAL modules resist up to ~20 fb-1  LS3
Innermost ECAL modules around beam-pipe can be replaced
Impact of pile-up on the energy /
position measurement:
Change the reconstruction and define
smaller clusters

## Slide 32: Particle ID with the Muon System
High detection efficiency: ε(μ) = (97.3±1.2)%
Low misidentification rates:
ε(p → µ) = (0.21 ± 0.05)%
ε(π→ µ) = (2.38 ± 0.02)%
ε(K→ µ) = (1.67 ± 0.06)%
MWPC
Y1S
Y2S
Y3S
YnS → µ+µ ̶

## Slide 33: Muon System upgrade
Modifications due to higher luminosity and 40 MHz readout:
  remove M1 due to too high occupancies
  additional shielding behind HCAL to reduce the rate in the inner region of M2
  keep on-detector electronics (CARIOCA); already at 40 MHz readout
  new off-detector electronics for an efficient readout via PCIe40 R/O boards
on-detector electronics
off-detector electronics

## Slide 34: Summary and Conclusions
LHCb is producing world best measurements in the b- and c-quark sector due to its excellent detector performance.
By 2018 with ~8 fb-1 LHCb will find or rule-out large sources of flavour symmetry breaking at the TeV scale.
The LHCb upgrade is mandatory to reach experimental precisions of the order of the theoretical uncertainties.
An efficient and selective software trigger with access to the full detector information at every 25 ns bunch crossing will allow to collect the necessary ≥50 fb-1 within ~10 years.
The LHCb upgrade is fully approved, with the last TDR under review.
The detector upgrade to 40 MHz readout sustaining a levelled luminosity of 2 x 1033 cm-2s-1 at 25 ns bunch spacing is under preparation, to be operational at the beginning of 2020.