## Slide 1: ARM (and other non-x86 architectures?) @ Glasgow
Sam Skipsey (he/they)
[work mostly by Emanuele Simili, some by Dan Protopopescu + Dwayne Spiteri]

## Slide 2: NetZero (“Why Do We Care”)
NetZero
Reduce Scope-2
Reduce Scope-3
Reduce Power
Greener Power
Hardware Choice
Lower PUE
Newer Hardware
Supply Choice
Usage Pattern
Buy Lower Scope-3 HW
Hardware Lifetime
Hardware Choice
Usage Pattern
Some of these things are not under direct site control.
This talk
Carbon Inventory
Carbon Allocation
Measure Power Use
Life-Cycle Assessment
Benchmark Hardware
Carbon Model
Measure + Model + Monitor  Moderate
Capture
Offset
Reduce Volume
Software
Techniques
Precision
Scope-2: Indirect emission of CO2 due to power used.
Scope-3: (Embodied) CO2 emitted during the manufacture of hardware.
(This slide from David Britton’s CHEP plenary)

## Slide 3: History (2)
In 2014, CMS and LHCb both looked at ARM as an alternative arch… and found it was more power efficient (but not powerful enough)
In 2020, the first ARM machine entered the top 500, at the top!
(and Apple announced they were switching to ARM for new MacBooks)
Scaling for x86 also slowing (and Intel being comprehensively outperformed by AMD)
Type | (Events/min)/core | (Events/min)/watt
Exynos442 Prime (ARM) | 1.14 | 1.14
Dual Xeon L5520 | 3.50 | 0.23
Dual Xeon E5-2630L | 3.33 | 0.33
Condensed from
David Abdurachmanov et al 2014 J. Phys.: Conf. Ser. 523 012009
GamerNexus comparison of Desktop x86 energy efficiency
(https://gamersnexus.net/cpus/best-cpus-2024-intel-vs-amd-gaming-production-budget-efficiency)

## Slide 4: Top 500 over time…
Chart: Top 10 of the TOP500 List, by Architecture
| 36831 | 37196 | 37561 | 37926 | 38292 | 38657 | 39022 | 39387 | 39753 | 40118 | 40483 | 40848 | 41214 | 41579 | 41944 | 42309 | 42675 | 43040 | 43405 | 43770 | 44136 | 44501 | 44866 | 45231 | 45597
IBM POWER | 5 | 5 | 3 | 3 | 5 | 5 | 4 | 4 | 2 | 3 | 1 | 5 | 5 | 5 | 2 | 2 | 1 | 3 | 3 | 2 | 2 | 2 | 2
x86 (inc Xeon Phi) | 1 | 1 | 2 | 3 | 1 | 3 | 4 | 6 | 7 | 6 | 8 | 8 | 4 | 4 | 4 | 7 | 6 | 7 | 6 | 6 | 6 | 6 | 6 | 7 | 8
ARM | 1 | 1 | 1 | 1 | 2
DEC ALPHA | 1 | 2 | 4 | 2 | 1
Hitachi RISC | 2 | 1
HPE MIPS | 1 | 1
NEC SX-6 | 1 | 1 | 1 | 1
Itanium | 1 | 1 | 1
SGI | 1 | 1 | 1
Cell | 1 | 1 | 1 | 1
SPARC64 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Sunway | 1 | 1 | 1 | 1 | 1 | 1 | 1
ARM

## Slide 5: ARM at Glasgow
Technology adoption often requires a “first mover” to invest in a technology sufficiently to allow validation
In 2021, Glasgow began evaluating energy efficiency in its existing and potential CPU estate – led by Emanuele Simili
We also managed to get Ampere Altra test machines for initial evaluation of ARM energy efficiency…
Since then, we’ve invested in significant ARM CPU estate (more later), and continued to evaluate new x86 and ARM CPUs…

## Slide 6: Benchmarks + Machines
Single Benchmark | Threading | Lang
JetReconstruction.jl + FastJet | Single (SIMD) | Julia + C++
Composite Benchmark |  | 
HEPSCORE | Multi/whole node | C++, Python
Node Type | Node CPU
2*Xeon | 2 * Intel XEON 10-Core CPU E5-2630 v4
Milano | AMD EPYC 7643 48-Core Processor
2*Milano+GPU | 2 * AMD EPYC 7443 24-Core Processor + 2* NVIDIA A100 PCIe 80GB
2*Roma | 2 * AMD EPYC 7452 32-Core Processor
2*Milano | 2 * AMD EPYC 7513 32-Core Processor
2*Bergamo | 2 * AMD EPYC 9754 128-Core Processor
2*Genoa | 2 * AMD EPYC 9654 96-Core Processor
Siena | AMD EPYC 8534P 64-Core Processor
Q80 | Ampere Altra Q80-30
Max28 | Ampere Altra Max M128-28
Max30 | Ampere Altra Max M128-30
Grace | NVidia Grace 144-Core 480GB DDR5
AmperOne | AmpereOne 192-Core
2*Q80 | 2 * Ampere Altra Q80-30

## Slide 7: HEPSCORE
HEPSCORE is a composite benchmark, a statistical average of 9 sub-workloads representing “typical” WLCG tasks, across the 4 WLCG experiments.
It is developed by the HEPiX Benchmarking Working Group – see https://arxiv.org/abs/2306.08118 - and is now the official unit for WLCG resource pledges.
We are interested in the Power Efficiency – the HEPSCORE / Watt – which is equivalent to the number of Joules per Event for event-oriented workflows.
We measure the 75-95 quantile average power, as a robust estimation of power consumption under load.

## Slide 8
HEPscore/Watt
Using the new FoM (75-95% quantile average), we measure performance per watt as:
*
New this week,
thanks to BIOS IT
2017
2022
2020
2024
2022
2023
2022
2024
2022
2022
2023
2023
2024
Chart: HEP-Score vs. Power <75-95%>
| 211.7 | 384.7 | 730.1 | 446.3 | 486.9 | 1322.2 | 1389 | 324.89999999999998 | 309.89999999999998 | 349.9 | 424.1 | 835.2 | 570.1 | 538.5
 | 385.6528 | 1356.1607 | 1692.1967 | 1826.3467 | 1887.2207 | 7497.4875 | 6932.2979 | 1838.5244 | 1512.5914 | 2068.0849 | 2121.2939 | 4205.4335 | 3234.0468 | 2520.5962
AMD x86
ARM
AmpereOne result may be an underestimate – other work suggests large pages (64k) may improve performance further.
We were testing with conventional 4k pages.
Notes: (*) but, this is not the whole story: each machine runs at its highest frequency (conservative governor), and frequency directly affects power usage.
See next slide !

## Slide 9
Frequency Scan
2.80
CPU power draw is not linear on clock speed.
Underclocking a CPU changes its energy efficiency…
Notes: (!) see performance/watt of Max vs Grace …
NOTE: the x coordinate shows the nominal frequency, i.e., the frequency that has been set via ‘cpupower frequency-set’.
This does not always stay constant during the run, especially x86 have a high frequency turbo mode that is switched on/off depending on load.

## Slide 10
Heterogeneous Compute Cluster @ ScotGrid
Job manager
wn_x86
wn_ARM
wn_x86
wn_x86
wn_x86
wn_x86
wn_x86
wn_ARM
wn_ARM
wn_ARM
wn_ARM
wn_ARM
wn_ARM
wn_x86
wn_x86
wn_x86
ce01.gla.scotgrid.ac.uk
ce02.gla.scotgrid.ac.uk
ce03.gla.scotgrid.ac.uk
ce04.gla.scotgrid.ac.uk
jobs
x86 queue
ARM queue
~15k cores (ht)
~4k cores
We provide ARM resources at the our WLCG Tier2 cluster within our standard ARC-CE endpoints.
At the moment, ARM resources are mainly used by ATLAS… but anyone who wants to use them can submit jobs to the ARM queue.
Please let us know if you are interested!
Notes: ScotGrid Glasgow Compute Cluster

## Slide 11: Julia Benchmarks
FastJet is a well-known & optimised “jet clustering” library for HEP, in C++ . It operates on an event – consisting of many (n) trajectories – and provides methods for outputting “jets”, clusters of associated trajectories. This is computationally complex, especially as n increases.
JetReconstruction.jl is an implementation in Julia of (an increasing number) of FastJet’s algorithms, as a demonstrator for Julia as a useful language for HEP.
Relative performance of programming languages can change based on architecture – due to differences in the efficiency of their compilers targeting different instruction sets, and due to differences in how well the language itself maps to architectural tradeoffs (for ex. memory ordering models, SIMD width…)
Partly inspired by
“Productivity meets Performance: Julia on A64FX”
Mosè Giordano, Milan Klöwer, Valentin Churavy
arXiv:2207.12762v1 [cs.DC] 26 Jul 2022
Another Fugaku powered ARM performance paper,
with Julia!

## Slide 12: Julia Results
ARM
ARM
Julia implementations are faster than C++
On both x86 and ARM
But there are significant differences in the degree…

## Slide 13: The future?
At present, ATLAS allow pledging of 50% of their CPU resources as ARM at a site.
Glasgow has a significant ARM estate – which was also used to validate ATLAS workloads to allow the above.
ARM offerings were initially more energy efficient than (all) x86
  Now (AMD) x86 is in a competitive cycle with ARM providers
  This is good for us, as there is now pressure on both sides to improve.
We remain interested in any other challengers – RISC-V is not there yet…
  …but both China and Europe have interest in developing it as a competitor.

## Slide 14: Questions?

## Slide 15
Milk-V Pioneer
~2.5k € from China
128 GB RAM, 64 cores desktop-class PC
Preliminary look at RISC-V
As the standard HEP benchmarks are not available on RISC-V, we used standard Geant4 detector simulation on the RISC-V and other 3 types of hardware (desktop i5, AMD EPYC and ARM Ampere Q80).
Notes: RISC-V will improve!
Already comparable to a mid-range x86 from 2017
Will soon become comparable with ARM
We wish to have a test-suite ready to follow the evolution …

## Slide 16: Questions?