## Slide 1: How Jisc is supporting End to end network monitoring with on the Janet network
Chris Walker (Jisc)
Duncan Rand, Raul Lopes, Tim Chown (Jisc)
IRIS Collaboration meeting 3rd December 2024

## Slide 2: Jisc’s network performance test facilities
Open to our members, and their collaborators, to use
perfSONAR
  10G (Slough) and 100G (London)
  Mesh and archive
Iperf and ethr
  10G - (100G on request)
10G data transfer node (DTN) for application-oriented disk-to-disk tests (100G coming)
All facilities
  IPv4/IPv6
  Jumbo frames (MTU=9000)
  TCP-BBRv3
See https://www.jisc.ac.uk/guides/using-the-janet-network-performance-test-facilities
Email netperf@jisc.ac.uk for any assistance or advice

## Slide 3: perfSONAR network monitoring
Matrix of tests
Jisc (https://ps-mesh.perf.ja.net/grafana/)
  Mesh configuration
  Visualisation / archive of results
Bandwidth (automated iperf ~6hrs)
One way Latency
Packet loss
Traceroute

## Slide 4: Performance Example 1
ps-london (100G) to a RAL Jasmin/SKA node
See here.
Excellent single stream performance (Top)
  RAL -> London steady
  London -> RAL less stable
Performance testing (Bottom)
  Drop due to testing
    Net.core.optmem_max= 1M

## Slide 5: Performance Examples 2
Sheffield
To: 9Gb/s
From: 0.1Gb/s
  Issue: Asymm routing
Liverpool
~1-2Gb/s
  Issue: Asymm routing

## Slide 6: Performance Examples 3
Glasgow
To: good
From bad
  Routing
~10Gb/s
Improvement to with detuning of 100Gbit transmission
Durham

## Slide 7: Performance 4
Lancaster
100G link causes performance decrease (below L) but why?
  100G Jisc node detuned (Top R) increase 3->15 Gb/s (Top R)
  10G Jisc node ~10Gb/s (Mid R)
  100G QMUL ~3Gb/s (Bottom R)

## Slide 8: Joining the Jisc Mesh
How?
  e-mail netperf@jisc.ac.uk and ask
  psconfig remote add https://ds2-london.perf.ja.net/psconfig/ds2-psconfig.json
Why?
  Measure network performance end to end.
  Facilitates debugging
    Found and fixed various issues
  Jisc has helped to correct
    Asymmetric routing
    TCP tuning
    IPv6 config, DNS config

## Slide 9
Christopher J. Walker
Christopher.Walker@jisc.ac.uk
netperf@jisc.ac.uk