## Slide 1: Getting the best out of Jisc's Janet network
Christopher J. Walker

## Slide 2: Overview
Janet Upgrades
  Optical upgrades
  Core Network upgrades
Network Performance
  Testing tools
  perfSONAR

## Slide 3: Janet Upgrades
Optical backbone (Ciena)
Deployed 12 years ago
  100G with 50GHz Channel width
    88 channels (8.8 Tbps)
    Fixed filters
    C band (1550nm)
Upgrade to colourless add/drop
  Wavelength Selective Switches (WSS) -> Flexgrid (done)
  DWDM (to do)
    Will give 400G /800G capability (75 GHz) – 23 Tbps

## Slide 4: Janet Upgrades
Routers
Core router upgrade
  Next couple of years
    400/800G likely
    Coherent optics?
    Southern network to go to 1.6 Tb (4*400G or 2*800G)
    Significantly less power

## Slide 5: Joiner – Telecoms research and NDFF
Joiner - Layer 2 overlay network
Federated testbed for telecom ecosystem research, fostering sharing of experimental resources and introducing new technologies.
Dublin node being added (with HEANet)
National Dark Fibre Facility (NDFF)
  Fibre for photonics/quantum etc

## Slide 6: Global links
Geant (European NRENs)
  Submitted EuroHPC hyperconnectivity bid (EU27) for Terrabit connectivity
Global R&E Networks (GREN)
  Optimised for low loss – for large science flows

## Slide 7: Thoughts
What does this unlock
Move data to compute
  On demand
  Real time
Location of compute
  Move compute rather than electricity
Storage federation
  Can’t get faster than the speed of light (in glass)
Time / frequency services
Fibre Sensing
Potential capability

## Slide 8: Network performance test facilities - Jisc
Slough and London
  IPv4/IPv6
  9000 MTU
Iperf (iperf2/3)
RIPE Atlas Anchor
100Gbit Data Transfer Node
  Delivered on Monday
    Installation soon
    Globus
      What else do people want?

## Slide 9: perfSONAR
HPC mesh
netperf@jisc.ac.uk to join
Latency/bandwidth monitoring

## Slide 10: perfSONAR
Custom Dashboards
XLZD mesh
Time Synchronisation mesh

## Slide 11: Jumbo Frames
Jumbo Frames = MTU=9000
Durham requested Jumbo Frames
  “Writing the tickets took longer than the change” (Jisc colleague)
    Jumbo frames across campus took longer.
  perfSONAR shows a (small) difference
    Capped by link (single stream max 10Gbit)
  Globus
    TBC

## Slide 12: perfSONAR
Time Synchronisation
Chrony.conf changes:
server ntp5.ja.net minpoll 5 maxpoll 5 iburst
  # Previously default minpoll/maxpoll 6
lock_all
Sysconfig: vm.swappiness from 60 to 1

## Slide 13: Jisc Communities
Research network engineering (RNE) community group – Jisc
Digital research community group – Jisc
Networkshop community group – Jisc *NEW*
Cyber security community group - Jisc

## Slide 14
Christopher J. Walker
Research Support Senior Manager
Christopher.Walker@jisc.ac.uk