Reduction of extraction losses with
barrier buckets in the PS
Mihaly Vadai
Acknowledgements:
A. Alomainy, H. Damerau, M. Giovannozzi, A. Huschauer, A. Lasheen, K. Mehran

---
Contents
- Measurements with beam:
  - Validation
  - MTE + barrier buckets
  - Loss reduction
- Concept of SPS synchronisation
- Conclusions
- Introduction:
  - Motivation
  - Extraction of fixed target beams
  - Interaction between beam and RF
- Implementation:
  - Wide-band waveform generation
  - FPGA Firmware
  - Installation

---
The CERN Accelerator Complex
- Chain of particle accelerators.
- Collider experiments and fixed target experiments.
- Current studies: fixed target beams for the SPS North Area. (NA58,60,61,62,63 and 64 https://greybook.cern.ch/)
  - Linac 4: 0 – 160 MeV (kinetic)
  - Proton Synchrotron Booster (PSB)
    160 MeV – 2 GeV (kinetic)
  - Proton Synchrotron (PS)
    2 GeV (kinetic) – 14 GeV/c (FT), 26 GeV (LHC)
  - Super Proton Synchrotron (SPS)
    14 GeV/c – 400 GeV (FT), 26 GeV – 450 GeV (LHC)
  - North Area fixed target experiments
- Intensity increase requires beam loss reduction.
- Non-negligible beam loss at PS extraction

---
North area
France
Prevessin
LHC
SPS
TT2
GVA airport
Meyrin
Switzerland
PS

---
Motivation
- Particle trajectory has to be changed from circular to the extraction trajectory.
- This is achieved using extraction devices, such as kicker magnets.
- These have a finite rise time and pulse length.
- During the rise time, the beam is swept. Leads to beam loss.
- The aim of the barrier bucket is to generate a gap in the beam while the field of the kickers build up 200-300 ns.

---
PS Multi-Turn Extraction 1
- The circumference ratio would require 10 or 11 transfers from PS to SPS -> would be very inefficient.
- Split beam transversely into a helix (multiple cork screws) to make a beam with a length of 5 PS turns.
- Two extractions from PS-SPS.
Operational performance of the CERN injector complex with transversely split beams
S. Abernethy, A. Akroh, H. Bartosik, A. Blas, T. Bohl, S. Cettour-Cave, K. Cornelis,
H. Damerau, S. Gilardoni, M. Giovannozzi, C. Hernalsteens, A. Huschauer, V. Kain,
D. Manglunki, G. Métral, B. Mikulec, B. Salvant, J.-L. Sanchez Alvarez,
R. Steerenberg, G. Sterbini, and Y. Wu
CC-BY Phys. Rev. Accel. Beams 20, 014001 https://doi.org/10.1103/PhysRevAccelBeams.20.014001

---
PS Multi-Turn Extraction 2
- 5 beamlets: 4 islands and 1 core extracted in 5 turns.
- Fills 5/11 of the circumference of the SPS.
- 2 acceleration cycles in the PS fill 10/11 of the SPS
- The remainder 1/11 is kept beam free for the rise times of the extraction kicker of the SPS.
- SPS is instructing the PS when to extract. Important for synchronisation.

---
RF interacting with particles
- Energy kick to particles at each turn at a cavity.
- Changes the next arrival time and energy.
- E0, T are constant for the same bending field.
- Results in periodic oscillations similar to of a pendulum.

---
Mechanical analogy: pendulum for bucket with sinusoidal RF voltage
- Pendulum in a gravitational field.
- Point like bobs on a mass-less, rigid rod. (No rotation, only translation.)
- Periodic motion: restoring force ∼ sin φ.
- Momentum (p) plotted for every angle (φ) for a motion with a given maximum potential energy (height).
- Closed trajectories up to the separatrix.
- p - φ phase plane plot also called phase space.

---
Mechanical analogy: extended pendulum for barrier buckets
- Point like bobs on a mass-less, rigid rod. (No rotation, only translation.)
- Friction-less track.
- Reflection is the same as a normal pendulum.
- Drift region or drift space introduced:
  - period made much longer
- Going to a synchrotron:
  - RF voltage during reflection ∼ sin φ
  - RF off – drift – no energy change.
  - Same non-linear effect on a charged particle as on a bob.
  - One limit of analogy: does not cover acceleration.

---
Conventional buckets
- Generated by single harmonic, narrow band waveform
- Single harmonic RF buckets
- Typical RF structures in a synchrotron.
- Well suited for acceleration, because high power can be delivered over narrow RF bands to the beam.

---
Barrier buckets
1 turn
- Generated by a multi harmonic, wide-band waveform.
- Two main parts:
  - Reflection region – beam loss reduction
  - Drift space – ideally flat longitudinal beam structure.

---
The instrument of gap making: PS Finemet cavity
- A wide-band (400 kHz −∼10 MHz) cavity already installed in the PS in 2014.
- Original purpose: kicker for the coupled-bunch feedback.
- Allows to generate signals with large bandwidth at cavity gap:
  - non-sinusoidal RF waveforms are possible.
- What else is needed?

---
Main challenges 1: RF drive needed
- Generating the wide-band, isolated pulse at the cavity gap.
- The power system distorts a pulse applied at the input: pre-distortion scheme needed.
- Beam synchronous generation of the barrier pulse.
  - Correct frequency and phase.
- Control: remote and beam synchronous pulse control (multiple pulses per turn, amplitude and phase).

---
Main challenges 2
- Full validation of the PS barrier bucket system with beam.
- Test handover options from conventional RF to barrier RF.
- Combination of two complex beam manipulations:
  - barrier bucket;
  - transverse splitting and 5-turn extraction.
- Priorities driven by the accelerator schedule.
  - Fast hardware implementation needed.
  - All measurements with beam had to be obtained before the beginning of LS2.
- SPS synchronisation scheme to be conceived.

---
Generation of single, sinusoidal pulses at the cavity gap.
- Compensation is needed for the system frequency response.
- Achievable pulse length is limited by the system bandwidth.
- Pulse width relates to usable gap size: 150 ns − 300 ns
  frev = 476 kHz (flat-top)

---
Beam synchronous arbitrary waveform generator
- Programmable azimuth with respect to circulating beam.
- Two pre-distorted pulses per turn with real time azimuth control.
- Amplitude modulation.

---
Barrier bucket LLRF and cavity installation

---
Proof-of-principle measurements at injection
- One potential barrier per revolution.
- Injection energy: Ekin = 1.4 GeV.
- Low intensity: Nb = 1×1011 ppp
  - Negligible beam induced voltage.
- Overlay of two measurements:
  - Injecting to the left and to the right hand side of the barrier.
- Demonstrated reflection of
  particles at barrier.
Consecutive turns

---
Controlling bunch length with moving barriers
- Stretching sinusoidal bucket to a barrier bucket.
- Longitudinal profile evolution during bunch length stretching.
- Validation.
Measured
Simulated

---
Conventional buckets to barrier bucket at flat-top
- 14 GeV/c momentum, nominal MTE without splitting. Getting closer to foreseen operational conditions.
- Wide-band, barrier bucket RF amplitude (blue) increased
- Main, h = 16 RF amplitude lowered (red)
- Potential barrier must be placed between
  h = 16 buckets to preserve quality.
- Shoulder formation observable especially at lower intensities.

---
Combination with MTE
- Longitudinal profile just before the 5-turn extraction.
- After extraction in the transfer line between the PS and SPS: 5 islands with gaps observed.
- Experimental demonstration that the barrier bucket scheme works together with the 5-turn extraction
- Note: 200 MHz modulation observable in the profiles is needed to ease the RF capture in the SPS. Short duration, little effect on beam dynamics.
SPS
TT2
PS

---
Loss reduction at PS extraction
- Kickers synchronised with PS internal signals, therefore with the barrier bucket system, too.
- Beam-loss monitors (ionisation chambers) along the ring.
- Beam-loss in the extraction region significantly reduced (log scale) in the probed intensity range in the extraction region.
- Loss-free Multi-Turn Extraction.
- Next step: synchronise with SPS.
Barrier bucket and transversely split beams for loss-free multi-turn extraction in synchrotrons
M. Vadai, A. Alomainy, H. Damerau, S. Gilardoni, M. Giovannozzi and A. Huschauer
2019 EPL 128 14002, DOI: 10.1209/0295-5075/128/14002

---
Synchronisaiton with the SPS

---
The need for synchronisation with SPS
Difference in time to be reduced to ~0.
- Kickers triggered on SPS signals, not PS.
- Comparison of the sum of the 5 turn longitudinal profiles to the 1 turn profile before extraction.
- Systematically present additional gap in the profile evolution.
- Gap made by the PS extraction kicker.
- Barrier RF in the PS was not yet synchronised with the SPS, while the kickers were. Need for SPS synchronisation scheme.

---
How to synchronise?
- Barrier to be placed between two bunches for symmetry reasons 16 possible positions.
- Extraction position required by SPS. (Kicker trigger.)
- In the best case beam only needs to be displaced by 2π/32 in azimuth back or forth.
- For the present concept the double 2π/16 is assumed. Assuming beam control does not allow bi-directional movement.
- Changing the length of the orbit by changing the RF frequency.

---
When to synchronise?
- The bunches have to be moved:
  - The closer to extraction the better (lower error in position).
  - Either during MTE or before.
- The mean energy of the beam has to be changed in a short time not to lengthen the cycle. → Efficiency.
- Sufficient RF power is needed.
- RF power only available before start of the MTE.
- Acceleration or deceleration has to take place earlier in the cycle not at extraction.

---
Steps in synchronisation
- Establish pre-conditions in synchronisation – matching RF frequencies:
  - Smooth switch from B-train frequency reference to SPS RF reference.
  - Reduce phase and radial loop gain to zero.
  - PS RF open-loop frequency is synchronous with SPS RF.
- Move bunches to the nearest possible gap position:
  - Perform phase measurement.
  - Program and perform phase bump by acting on the master clock frequency.
  - Gap between bunches in the right position.
- Barrier bucket and transverse splitting:
  - Reduce main RF voltage and perform transverse splitting.
  - Set barrier azimuth position synchronously with the extraction kickers.
  - Gap made by the barrier is between bunches and synchronous with the kickers.
- Trigger beam transfer.

---
Simulating the phase bump
- 2π/16 phase displacement shown for 1 bunch.
- The 12 ms time is too short to preserve the beam quality.→ Oscillations, as also predicted by analytical calculations.
- 30 ms much better.
- Time difference during the phase slip of the bunch position and programmed position.
- Final oscillations in the same order as initial matching error for more than 30 ms duration.

---
Conclusions
- Concept of beam loss reduction using a barrier bucket introduced.
- Beam synchronous waveform generator hardware design with pre-distortion conceived, implemented and validated with beam.
- Barrier bucket proof of concept measurements with beam.
- Combination with the Multi-turn Extraction achieved.
- Significant beam loss reduction in the PS proven across the probed intensity range.
- SPS synchronisation concept developed.

---
Next steps
- Accomodate the synchronisation procedure in the fixed target cycle in the PS.
  - Elaborate on the details of frequency handover and phase measurement.
- Optimisation of the PS fixed target cycle, especially the de-bunching porcess.
- Assess the impact of the gaps on the SPS performance.
  - Analyse SPS fixed target cycle with and without gaps.
- More measurements with beam to assess the overall performance.

---
Thank you for your attention